## Slide 1: Cladding attachment

## Slide 2: Foam Plastic Insulating Sheathing (FPIS) Products:
Exterior wall coverings are attached directly through the FPIS into the framing or to furring attached through the FPIS to framing.
Shall be installed in accordance with:
  Code compliance requirements per TER 1303-04
  How to Install FPIS Installation Guide
  Manufacturer’s installation instructions
  The following general installation guidelines

## Slide 3: Step 1: Verify FPIS and Framing
FPIS must have min compressive strength of 15 psi
Must comply with ANSI/SBCA FS100 where wind pressure resistance is required
ASTM D 1621
+
_
_
Note: Wind speeds shown in Table 1 are VASD. Where VULT is used, multiply wind speeds by a factor of 1.26

## Slide 4: Step 1: Verify FPIS and Framing
Wood framing may be any softwood species with specific gravity 0.42 or higher
Steel framing must be:
Thickness | Minimum Fb
33 mil, 43 mil | 33 ksi
54 mil | 50 ksi
Fb

## Slide 5: Step 2: Verify Fasteners
Exterior coverings may be attached by the following methods:
Cladding
Fasteners
Furring
FPIS
Framing
Cavity Insulation
Interior wall finish
Direct Attachment
Attachment through Furring
(a)
(d)
(a)
(c)
(d)
(e)
(f)
(g)
(e)
(f)
(g)
(b)
(b)

## Slide 6: Step 2: Verify Fasteners
Fasteners must meet penetration requirements per IRC Table R703.3(1) into:
  Studs
  Framing members
Where penetration into framing is not required, fasteners must extend ¼” beyond the opposite face of the sheathing per IRC Table R703.3.2
1¼” min
or per manuf.
instructions
1/4” min

## Slide 7: Step 3: Place Insulation Boards
Ensure wall is square and true
Align boards with bottom edge of wall

## Slide 8: Step 3: Place Insulation Boards
Verify stud spacing, blocking, and bracing requirements with manufacturer.
Provide framing or blocking for attachment of siding and trim at transitions
  Seams should not be visible from interior unless allowed by manufacturer.
16” o.c. (or per
manuf.)

## Slide 9: Step 4: Attach Insulation Boards
Space fasteners per manufacturer’s instructions
  Around edges of panel
  Through panels and into interior members
Edge Spacing
Interior Spacing

## Slide 10: Step 4: Attach Insulation Boards
Drive nails flush and snug
Do not over drive nails
Do not under drive nails
  Exception: Leave 1/32” gap (or as required by manufacturer) to allow for lengthwise thermal expansion of vinyl or aluminum siding

## Slide 11: Step 5: Trim Boards at Openings
Trim boards at all window and door openings
Cover all framing with FPIS
Fit joints tightly
FPIS Continuous Insulation

## Slide 12: Step 6: WRB and Flashing
Ensure that a code-compliant water resistive barrier (WRB) and required flashing is provided
If using FPIS as a WRB:
  Seal all joints and openings and penetrations per manufacturer’s installation instructions

## Slide 13: Step 6: WRB and Flashing
At pipe and other small penetrations, seal gaps with silicone or expanding spray foam sealant
Seal joints and openings with joint tape per manufacturer’s instructions
  FPIS
  Continuous Insulation

## Slide 14: Step 6: WRB and Flashing
Repair damaged areas per manufacturer’s instructions